## Slide 1: CSE160 - Project #1
TA: Ashish Yadav
Email: ayadav6@ucmerced.edu

## Slide 3: Flooding
One of the simplest methods of multi-hop communication
Also one of the most inefficient one-to-one protocol
  The bubble sort of Networks
Has no knowledge of the topology

## Slide 4: Sending a Letter using Flooding
I want to send to a letter to my pen-pal in New York, but I don’t have his address.
The solution is easy, I’ll use the protocol I learned in Networks
I make multiple copies of the letters and give it to my friends
Whenever they receive a letter, if it is not for them they make a copy and give it to all of their friends
Continue to do this until the letter is received at the final destination
https://en.wikipedia.org/wiki/Six_degrees_of_separation

## Slide 5: Flooding
A
B
C
D
E
F
Send packet from point A to F.
Notes: Here is a diagram of a simple network. Our goal is to send a packet from the Node A to Node F.
We begin by broadcasting from A. This packet will be received by both B and C. Both B and C are not the intended recepients so they sent it to all of their neighbors. Notice at this step, A receives the same packet from C and B. Since A has seen this packet, and it is the original sender, it will not rebroadcast it. D and E have not seen the packet so it will broadcast the packet to its neighbors. D and E broadcast the network with the packet and B, E, C, and F all receive the packet. B, E, and C have seen the packet so it can drop the packets. F is the intended recepient and will process the recieve data.

## Slide 6: Flooding Notes
A few key problems:
  Question: How do we track packets we have seen?
  A Solution: Using a sequence number and source information
  Question: How do we know when to give up?
  A Solution: Having a maximum time to live (TTL) : Time to live (TTL) or hop limit is a mechanism that limits the lifespan or lifetime of data in a computer or network.

## Slide 7: Neighbor Discovery
Neighbor discovery is built on flooding
You are looking for your immediate neighbors
B
C
A
D

## Slide 8: TinyOS - Mini-Guide

## Slide 9: Quirks of TinyOS
No dynamic allocation. E.g. malloc()
Breaking up large functions into smaller loops
Processor is not powerful
  No hardware floating point operations

## Slide 10: Interfaces
Similar to headers in C and C++
SimpleSend.nc
#include "../../includes/packet.h"
interface SimpleSend{
command error_t send(pack msg, uint16_t dest );
}

## Slide 11: SimpleSendP.nc - Module Header
module SimpleSendP{
provides interface SimpleSend;
uses interface Queue<sendInfo*>;
uses interface Pool<sendInfo>;
uses interface Timer<TMilli> as sendTimer;
uses interface Packet;
uses interface AMPacket;
uses interface AMSend;
uses interface Random;
}
Notes: Keywords! Module, this means that this code will programmatically implement an interface. Provides interface means that we will be implementing the functions that were stated in the interface section. Uses means that the interface will be used here and needs to be wired by a configuration. There is a concept of templates, like C++, here. Notice that Queue<sendInfo> is being used. You can change this out to a different type.

## Slide 12: SimpleSendC - Configuration
#include "../../includes/packet.h"
configuration SimpleSendC{
provides interface SimpleSend;
}
components as App;
SimpleSend = App.SimpleSend;
components new TimerMilliC() as sendTimer;
components RandomC as Random;
components new AMSenderC(AM_PACK);
App.sendTimer -> sendTimer;
App.Random -> Random;
App.Packet -> AMSenderC;
App.AMPacket -> AMSenderC;
App.AMSend -> AMSenderC;
//Lists
components new PoolC(sendInfo, 20);
components new QueueC(sendInfo*, 20);
App.Pool -> PoolC;
App.Queue -> QueueC;
}
Notes: Configuration means that the implementation will contain information on how it is wired. If this is meant to be the main class, you can further pass the provide. Keywords, Implementation is the block where we will be doing the wiring.
components is used to declare an object. Notice how some of them say new, this is because there can be multiple instances of these types. For the most part you will be dealing with singletons. Notice RandomC is a singleton. You don’t need to make a new instance of random every time you use it. A new timer is made since you may want different timers going at once. Similar to PoolC and QueueC.
We can use the “as” keyword to name the component.
Notice how we wire everything that was declared in SimpleSendP. We make all of the components and wire it in this configuration. This is done with a dash and greater sign. The arrow can flipped the other way. This is true for all of them except for the interface we are providing. Here we use an equal sign. An equal sign is used to denote that someone else is taking care of the implementation.

## Slide 13: Sending
error_t send(uint16_t src, uint16_t dest, pack *message){
if(!busy){
pack* msg = (pack *)(call Packet.getPayload(&pkt, sizeof(pack) ));
// This copies the data we have in our message to this new packet type.
*msg = *message;
if(call AMSend.send(dest, &pkt, sizeof(pack)) ==SUCCESS){
busy = TRUE;
return SUCCESS;
}else{
dbg(GENERAL_CHANNEL,"The radio is busy, or something\n");
return FAIL;
}
}else{
dbg(GENERAL_CHANNEL, "The radio is busy");
return EBUSY;
}
}

## Slide 14: Sending
event void AMSend.sendDone(message_t* msg, error_t error){
//Clear Flag, we can send again.
if(&pkt == msg){
busy = FALSE;
postSendTask();
}
}
}

## Slide 15: Conclusion
There is a lot of information provided here, but there is a ton more documentation out there.
  Read parts of the Tinyos Programing Guide by Phil Levis and David Gay
Next step I am going into is the structure of the code
Any Questions?